## Slide 1
LESSON 02
Dosimetric Quantities
PPT 2 - 1
NDRF | CBRN | INDIA
CBRN Module: Radiological-Nuclear
Presented By:- Kamal Mehra,2IC

## Slide 2
Upon completing this lesson, you will be able to:
OBJECTIVES
  Acquaint with various types of Dosimetric quantities and their units
  Define absorbed dose, equivalent Dose and effective dose and know its uses
  Acquaint with CPM and CPS and its importance.
1
2
3

## Slide 3
Upon completing this lesson, you will be able to:
OBJECTIVES
  Know About annual dose limitation Derived Air Concentration.
4

## Slide 4
Dosimetric quantities are specific measurements used in radiological protection to quantify the amount of radiation energy absorbed or transferred within a material, such as the human body.
DOSIMETRIC QUANTITIES

## Slide 5
REQUIREMENT AND IMPORTANCE OF QUANTIFYING DOSIMETRIC QUANTITIES
Risk Assessment and Emergency Response Planning
Regulatory Compliance
Operational Decision Making and Execution
Post-Incident Monitoring
Scientific Research
Medical and Industrial Use
Environmental Monitoring

## Slide 6
CATEGORIZATION OF DOSIMETRIC QUANTITIES
Dosimetric Quantities
Physical Quantities
Operational Quantities
Protection Quantities

## Slide 7
The activity of a radioactive material is a measure of its spontaneous transformation. It is defined as the number of disintegrations or transformations that take place per unit time.
The quantity (intensity) of radiation released from a radiation source is proportional to its activity.
The unit of activity is Becquerel (Bq).
1 Bq= 1 disintegration per second (1dps)
The old unit of activity is Curie (Ci).
1 Ci= 3.7x1010 disintegration per second
PPT 2 -
Physical Quantities
Activity λ

## Slide 8
The energy of radiation refers to the amount of energy carried by individual radiation particles or photons.
The energy of radiation is a critical factor in determining its ability to ionize matter and cause biological damage. High energy radiation generally poses a greater health risk than low energy radiation.
It is conventionally measured in Electron volt (eV) or Joule (J).
01 eV = 1.602 Eˉ¹⁹ Joules
1000 eV = 1 keV
PPT 2 -
Physical Quantities
Energy (E)

## Slide 9
Exposure is a fundamental Dosimetric quantity used to measure the amount of X-ray or gamma radiation at a specific point of interest.
Exposure quantifies the amount of electric charge (in coulombs) generated per kilogram of air due to the ionization caused by radiation.
The unit of exposure in the International System (SI) is coulomb per kilogram (C/kg) and traditional unit is Roentgens per hour.
The conversion between the traditional and SI units of exposure can be expressed as - 1 C/kg = 3,381 R
PPT 2 -
Physical Quantities
Exposure (X)

## Slide 10
KERMA is a measure of the amount of total energy transferred by photons (X-rays or gamma rays) interacting in the medium.
Kerma is an important concept in radiation dosimetry, particularly for high-energy photons and neutrons. It provides an estimate of the energy transferred from the radiation field to the irradiated material.
Kerma is expressed in joules per kilogram (J/kg). SI unit of Kerma is Gray (Gy).
1 Gy=1 J Kg-1
PPT 2 -
Physical Quantities
KERMA (Kinetic Energy Released in Matter)

## Slide 11
Ambient Dose Equivalent is defined as the equivalent dose at point P at a depth of d mm in the ICRU-sphere.
The corresponding unit is sievert (Sv).
PPT 2 -
Operational Quantities
Ambient Dose Equivalent {H*(d)}

## Slide 12
The directional dose equivalent is one of the operational quantities defined for use in area monitoring against external exposures.
The unit of directional dose equivalent is joule per kilogram (J Kg-1)
PPT 2 -
Operational Quantities
Directional Dose Equivalent {H' d,Ω}

## Slide 13
The operational dose quantity personal dose equivalent (Hp(d)) is defined as the equivalent dose in soft tissue at a suitable depth under a specified point on the body.
The corresponding unit is sievert (Sv).
PPT 2 -
Operational Quantities
Personal Dose Equivalent {Hp(d)}

## Slide 14
Absorbed dose is the amount of energy deposited by ionizing radiation per unit mass of irradiated matter such as tissue.
Absorbed dose is a fundamental quantity in radiation protection and is used to assess the potential for radiation induced biological effects.
Traditional unit of Absorbed Dose is RAD.
1 RAD=0.01 joules/Kg (J/Kg)
SI Unit of Absorbed Dose is Gray (Gy).
1 Gy=100 RAD
PPT 2 -
Protection Quantities
Absorbed Dose (D)

## Slide 15
Equivalent dose is a measure of the biological effectiveness of different types of ionizing radiation.
This is taken to account by multiplying the absorbed dose by a suitable weighting factor. This factor is known as Radiation Weighting Factor, Wᵣ.
The weighted absorbed dose is called Equivalent dose HT
The unit of equivalent dose is Sievert (Sv)
HT = WR * DTR
Traditional (old) unit of equivalent dose is REM (roentgen equivalent man) and the new unit is Sievert (SV), where 1Sv = 100 REM.
PPT 2 -
Protection Quantities
Equivalent Dose (H)

## Slide 16
RADIATION WEIGHTING FACTOR

## Slide 17
EQUIVALENT DOSE : IMPORTANT POINTS
If the absorbed dose from  is 1Gy ; equivalent dose is 20 Sv.
If the absorbed dose from  is 20Gy ; equivalent dose is 20 Sv.
Hence in terms of biological damage 1Gy of  dose is equivalent to 20Gy of  dose.

## Slide 18
Effective dose is a measure of the overall health risk associated with exposure to ionizing radiation. It accounts for the different sensitivities of different organs and tissues to radiation.
The sensitivity of different tissues to radiation is different. A number of organs are considered on the basis or their sensitivity and the seriousness of the damage. Risk factors are age and sex dependent.
PPT 2 -
Protection Quantities
Effective Dose (E)

## Slide 19
The Effective dose is computed by multiplying the tissue dose by a Tissue weighting factor (WT) appropriate to the tissue.
  Effective Dose(E) =  WT* HT
  Unit of effective dose = Sievert
  WT represents the contribution of tissue T to the total risk due to stochastic effects resulting from uniform irradiation of whole body.
PPT 2 -
Protection Quantities
Effective Dose (E)

## Slide 20
TISSUE WEIGHTING FACTOR

## Slide 21
SUMMARY OF DOSIMETRIC UNITS

## Slide 22
This indicates the number of radiation particles or photons detected by the instrument in one minute. It’s commonly used in handheld devices for environmental monitoring, as it smooths short-term fluctuations in radiation levels.
COUNTS PER MINUTE (CPM)

## Slide 23
This indicates the number of radiation particles or photons detected by the instrument in one second. It is used for measurements when higher count rates are being encountered, or if handheld radiation survey instruments are being used which can be subject to rapid changes of count rate when the instrument is moved over a source of radiation in a survey area.
COUNTS PER SECOND (CPS)

## Slide 24
Annual Limit on Intake, ALI, is defined as the activity intake (Bq) of a radionuclide which would lead to an effective dose corresponding to the annual limit.
ANNUAL LIMIT INTAKE (ALI)

## Slide 25
Concentrations of radioactive materials in air are limited by the Derived Air Concentration (DAC), which are derived from the ALI.
DAC denotes the max concentration of a radionuclide (or activity concentration) in the ambient air which, if inhaled by a person for 2000 hrs in a year, at a breathing rate 1.2 m3 /hr, will not result in annual effective dose equivalent in excess of the limits prescribed by the competent authority.
PPT 2 -
DERRIVED AIR CONCENTRATION

## Slide 26
THANK YOU